## Slide 1: RFID based online monitoring attendance system
Aman Ranjan Verma | Saurabh kumar | Sumit kumar
END SEM EVALUATION PRESENTATION
Dept. of Electronics and Communication Engineering, IIIT Manipur

## Slide 2: Introduction :
Radio Frequency Identification based attendance system is an automatic attendance system which consists of a micro controller, RFID reader, RFID tag and a data base(firebase) as its primary components.

## Slide 3: Motivation behind the project
Roll call in educational institutions and offices consumes considerable amount of time and resources.
Schools can overcome this inefficiency and address the problem adopting RFID based attendance.
Though this traditional attendance management is still popular in many of schools, the concept of the use of RFID based attendance system is gradually gaining momentum in city schools.
Child Safety is very important nowadays and everyone wants to get information from the school about their child attendance in the school.

## Slide 4: Problems of existing attendance systems
Earlier attendance system is based on GSM module.
  The setup cost and operating cost of these systems are more.
What’s new in our attendance system ?
Since, it uses Wi-Fi module for data transmission, it’s operational cost is almost zero.
Highly customizable
Highly scalable
Dedicated android application to keep track of the attendance record.
Graphical Display
It uses counters to avoid proxy.

## Slide 5: Started with Bidirectional counter

## Slide 6: Started with …
Earlier we started with MFRC522 which works on 13.5 MHz frequency.
But since our card works on 125 KHz, we had to switch to EM18 RFID module.

## Slide 7: EM18 RFID READER MODULE

## Slide 8: Working principle
As the RFID Reader is sending a radio waves of a particular frequency so the voltage that is induced across the coil is also of a particular frequency.
The magnetic field generated by RFID module induces current in RFID tag. This is called as inductive coupling.
According to the data that is stored inside this RFID Tag then that data can be read by the RFID Reader in the form of a voltage. So, in this way the data is sent back to the RFID Reader.
Further Arduino will receive the data and process it.

## Slide 9: Working principle cont …
125 KHz

## Slide 10: Interfacing

## Slide 11: Interfacing
Arduino – LCD

## Slide 12: Interfacing cont ..
Arduino --> Wi-Fi --> Firebase

## Slide 13: Arduino + Wi-Fi + Firebase

## Slide 14
Complete Circuit Diagram

## Slide 15: Android Application
IOT Based attendance system

## Slide 16: Android
Android is a mobile operating system developed by Google, based on a modified version of the Linux kernel and other open source software and designed primarily for touchscreen mobile devices such as smartphones and tablets.

## Slide 17: Android App

## Slide 18: Android App
Attendance System

## Slide 19: Attendance System App
Structure
  Layout
    Views
    Programmed using XML
Working
  Functionality
  Programmed using Java

## Slide 20: Attendance System App
Structure
  Layout
    Views
    Programmed using XML
Working
  Functionality
  Programmed using Java
Image View
Button View
Text View

## Slide 21: Attendance System App
Structure
  Layout
    Views
    Programmed using XML
Working
  Functionality
  Programmed using Java

## Slide 22: Attendance System App
Structure
  Layout
    Views
    Programmed using XML
Working
  Functionality
  Programmed using Java

## Slide 23: Attendance System App
Structure
  Layout
    Views
    Programmed using XML
Working
  Functionality
  Programmed using Java

## Slide 24: Attendance System App
Structure
  Layout
    Views
    Programmed using XML
Working
  Functionality
  Programmed using Java

## Slide 25: Attendance System App
Structure
  Layout
    Views
    Programmed using XML
Working
  Functionality
  Programmed using Java

## Slide 26: Attendance System App
Working
  Functionality
  Programmed using Java
Gmail

## Slide 27: Attendance System App
Structure
  Layout
    Views
    Programmed using XML
Working
  Functionality
  Programmed using Java

## Slide 28: Attendance System App
Structure
  Layout
    Views
    Programmed using XML
Working
  Functionality
  Programmed using Java

## Slide 29: Flow of Data from Arduino to App

## Slide 30: Flow of Data from Arduino to App cont..

## Slide 31: Firebase Security

## Slide 32: Project
Let’s move for demonstration.

## Slide 33: Thank You